## Slide 1: NHD: A Topology-Aware Kubernetes Scheduler
Cliff Burdick
Viasat
November 20, 2019

## Slide 2: Agenda
Terminology
01
HPC/NFV Requirements
02
What Is Topology Awareness?
03
Challenges With HPC/NFV Software In Kubernetes
04
NHD: A New Topology-Aware Scheduler
05
Future Work
06

## Slide 3: Similar Talks
Is There a Place for Performance Sensitive Workloads in Kubernetes?
  Today, • 3:20pm - 3:55pm (Room 15AB)
  Gergely Csatari & Levente Kale, Nokia
Mitigating Noisy Neighbours: Advanced Container Resource Management
  Today, • 3:20pm - 3:55pm (Room 28ABCDE)
  Alexander Kanevskiy, Intel
Running High-performance User-space Packet Processing Apps in Kubernetes
  Tomorrow, November 21 • 2:25pm - 3:00pm (Room 5AB)
  Abdul Halim, Intel & Peng Liu, Red Hat
RDMA Enabled Kubernetes for High Performance Computing
  Tomorrow, November 21 • 4:25pm - 5:00pm (Room 33ABC)
  Jacob Anders, CSIRO & Feng Pan, Red Hat

## Slide 4: Terminology
HPC (High Performance Computing)
  Software that performs calculations at a high speed on dense servers
  Typically uses accelerator cards
NFV (Network Function Virtualization)
  Virtualizing network functions in software
NUMA
  Non-Uniform Memory Access
RDMA
  Remote DMA – Transferring data directly from NIC to other device

## Slide 5: HPC/NFV Requirements
High Network Throughput
  40-100 Gbps Interfaces
  Multiple interfaces
  Tens of millions of packets per second
Low Latency
  < 10us packet processing time
SmartNICs
  HW offloads
  SR-IOV
Accelerator cards
  GPUs, FPGAs, TPUs, etc

## Slide 6: What’s Needed?
Userspace networking
DPDK
Isolated CPUs
NUMA-Awareness
Both memory and devices
RDMA
Used to transfer data directly from NIC to other devices
Hugepages
Larger page sizes for fewer TLB misses
All of these require some level of topology awareness!

## Slide 7: DPDK
Userspace packet processing framework
Completely bypasses kernel
  Most of the time
Polling-based
Dozens of poll mode drivers (PMDs)
  Allows users to change hardware without modifying the software
Provides NUMA-aware high-performance libraries
  Inter-thread communication
  Memory allocator
  Crypto
Foundation of many high-speed packet processing libraries

## Slide 8: DPDK Performance

## Slide 9: What does it mean to be topology-aware?

## Slide 10: Scheduling A Pod
2) Find Resources
(CPU, memory, disk)
1) Ready For Scheduling
3) Schedule Pod

## Slide 11: Single Socket, No Hyperthreading
Intel Xeon
Core
0
L
1
L
2
L3 Cache
•••
IO, PCIe, etc
Graphics
DDR Controller
Core
1
L
1
L
2
Core
19
L
1
L
2
DDR
80GB/s

## Slide 12: Single Socket, Hyperthreading
Intel Xeon
Core
0
L
1
L
2
L3 Cache
•••
IO, PCIe, etc
Graphics
DDR Controller
Core
20
Core
1
L
1
L
2
Core
21
Core
19
L
1
L
2
Core
39
DDR
80GB/s

## Slide 13: Dual Socket, Hyperthreading
Intel Xeon
Core
0
L
1
L
2
L3 Cache
•••
IO, PCIe, etc
Graphics
DDR Controller
Core
20
Core
1
L
1
L
2
Core
21
Core
19
L
1
L
2
Core
39
Intel Xeon
Core
0
L
1
L
2
L3 Cache
•••
IO, PCIe, etc
Graphics
DDR Controller
Core
20
Core
1
L
1
L
2
Core
21
Core
19
L
1
L
2
Core
39
UPI
80GB/s
80GB/s
35GB/s

## Slide 14: GPU + NIC
12.5GB/s
12.5GB/s
35GB/s

## Slide 15: Single-Root PCIe
12.5GB/s
12.5GB/s
35GB/s

## Slide 16: GPU + NIC + PCIe Switches
12.5GB/s
12.5GB/s
12.5GB/s
12.5GB/s
35GB/s

## Slide 17: GPU + NIC + PCIe Switches
12.5GB/s
12.5GB/s
12.5GB/s
35GB/s

## Slide 18: Network

## Slide 19: Kubernetes Challenges
Isolating Cores
CPU Selection
NIC/Interface Sharing

## Slide 20: Kubernetes Challenges
Isolating Cores
CPU Selection
NIC/Interface Sharing

## Slide 21: Isolating CPUs
Prevent unwanted processes from running on certain cores
User-spawned processes explicitly affine or “pin” to cores being isolated
Kernel processes are trickier
  Some threads cannot be moved
  Interrupts use a special configuration
Two ways to handle it

## Slide 22: isolcpus
Available in any kernel version
Linux boot parameter
Isolates a specific set of CPUs one time on boot
Some kernel processes do not follow isolation rules
Works alongside cgroups/cpusets
isolcpus=0,1,16,17

## Slide 23: cpusets
Added in kernel 2.6.24 (2008)
Created/modified any time after boot
Creates a group or set of CPUs that are allowed
All processes belong to a group
Hierarchical
Used by Kubernetes
By default, isolcpus settings are (kind of) ignored

## Slide 24: Our Solution: IsolCpusets
Host daemon isolates at runtime
Hooks into systemd before docker service
Creates isolated cpuset based on isolcpus setting
Creates jailed cpuset based on inverse of isolcpus
Moves interrupts to non-isolated cores
Moves all processes to jailed set
Pods needing isolation communicate with daemon
  Moves into isolated set

## Slide 25: Kubernetes Challenges
Isolating Cores
CPU Selection
NIC/Interface Sharing

## Slide 26: CPU Core Selection
For most applications, CPU core selection is unnecessary
  Linux handles this pretty well
NUMA/PCIe-aware applications need better
DPDK needs to know the physical core numbers when initialized
CPU Manager for Kubernetes allowed selection of cores from a group on a best-effort basis, but not physical numbers
Hyperthreading/SMT
  Not all cores are equal
Intel Xeon
Core
0
L
1
L
2
L3 Cache
•••
IO, PCIe, etc
Graphics
DDR Controller
Core
20
Core
1
L
1
L
2
Core
21
Core
19
L
1
L
2
Core
39

## Slide 27: Kubernetes Challenges
Isolating Cores
CPU Selection
NIC/Interface Sharing

## Slide 28: Sharing NICs
Easy without DPDK
Each pod runs in isolated network namespace
DPDK presents new problems
  Linux/iptables has no effect on packets
  Want to share interfaces without losing efficiency
Several different methods for sharing analyzed

## Slide 29: Sharing NICs: Virtual Switch
All pods communicate to virtual switch
  vhost/virtio-user
  SR-IOV
  memif
Switch is programmed with forwarding rules from external controllers
Flexible, fairly platform-agnostic
Can be inefficient, depending on interface
No RDMA support

## Slide 30: Sharing NICs: Multiple Queues
Pods attach to one or more hardware queues on the NIC
Requires assignment of queues to each pod
No overhead; pods send and receive directly to/from NIC
Not possible without host networking!

## Slide 31: Sharing NICs: Host-Device
Each pod owns one or more entire interfaces
Can utilize multiple queues on the device they own
Pods not needing to use full interface bandwidth prevent others from being scheduled there
Number of pods per node limited by number of interfaces per node

## Slide 32: Sharing NICs: SR-IOV
Each pod owns one or more virtual functions (VFs)
Unique MAC address per virtual function
Modern NICs support far more VFs than a node can hold pods
Very little overhead
VFs chain together to function as switch for intra-node traffic
Mature Kubernetes support
May not have the same flow capabilities as PF

## Slide 33: NHD: A Topology-Aware Custom Kubernetes Scheduler

## Slide 34: Why Make A Scheduler?
Latency/jitter requirements sometimes can’t be met without one
  One pod per node may solve this
  Most applications do not need to use all the resources on a node
Money
  Inefficient bin packing uses more resources
Allows for quicker changes compared to upstream
Photo by JP Valery on Unsplash

## Slide 35: NHD
Topology-Aware
  PCIe
  NUMA
  Hyperthreading/SMT
  GPUs
  Data plane NICs (with Multus)
  CPU/GPU architecture
  Helper versus data path cores
Written in Python 3
gRPC interface for cluster statistics
Features At A Glance
NHD

## Slide 36: NHD
Uses Node Feature Discovery + User Hooks for discovering hardware features
  Isolated CPUs
  GPUs: Generation, NUMA node, PCIe topology
  NICs: Interface names, speeds, NUMA node, PCIe topology
Uses Multus with either host-device or SR-IOV plugins for DPDK
Builds a generic topology structure agnostic to the application’s configuration
Schedules GPUs without Nvidia device plugin
  Need to select specific device based on topology
Chooses specific CPU cores based on application’s hyperthreading restrictions
Features At A Glance

## Slide 37: Algorithm
Pod Watch
Config Translation
Matcher
Config Translation
Bind

## Slide 38: Matcher
Finds best possible node for placement of current workload
Tries to pack as many pods onto a single node as possible before using another node
  Can’t predict the future
Matching Stages:
  Filter native pod resources
    Hugepages currently
  NUMA/PCIe filter
  Intersection of each resource meeting NUMA/PCIe constraints
Photos by Annie Spratt and Belinda Fewings on Unsplash

## Slide 39: Pod Resource Requests
Processing Group 2
Processing Group 1

## Slide 40: Node Matching
Single Pod, One Group

## Slide 41: Node Matching
Single Pod, One Group

## Slide 42: Binding
Best node has been chosen after matching stage
Issues a bind command to Kubernetes API server on pod object
Issues native Kubernetes events viewable from any standard monitoring system

## Slide 43: Upstream Topology Manager
First introduced in Kubernetes 1.16 as alpha
Uses topology hints from hint providers to map devices to other resources (CPUs)
Not part of the Kubernetes scheduler
  Runs in Kubelet on each node
Adding PCIe/other topologies support soon?

## Slide 44: Future NHD Work
Open source
  Going through legal currently
  https://github.com/Viasat/nhd
Intel’s Resource Directory Technology
  Cache/memory bandwidth segregation
Speed improvements
NVLink Topology
Delete project!

## Slide 45: Thanks
Viasat
  Tim Martin, Federico Calzamiglia + Signal Processing Team
  Piotr Siwczak
Intel
RedHat